## Slide 1
Level 0
Physical Process
Field I/O device
Railway Sensors
Railway Signals
Train Sensors
Train Moto
Train Brake
Level 1
Controller LAN
Railway PLC
Train RTU
Train PLC
Level 2
Control Center (HQ) Processing LAN
Railway Track Control HMI
Railway Train Control HMI
Level 3
Operations Management Zone
Management HMI
Application Server
Data Base Server
Historian Server
Engineer workstations
Domain Controller
Internal Web-Server
Business Server
Staff laptop/Desktops
Level 4
Enterprise
Zone
External Web-Server
Email Server
Level 5
Internet DMZ
Zone
Railway Track Control HMI
Railway Train Control HMI
Railway Physical World Simulator
PLC Simulator
RTU Simulator
Mini Railway Cyber Range (Railway [Metro] IT-OT System Cyber Security Test Platform)

## Slide 2
Corporate network [IT network]
Supervision network SCADA
Production network
Physical real world emulation network
Real world emulator
Track junction sensors-signals control emulators
Train station sensors-signals control emulators
Railway Trains emulators
Junction sensor-signal control PLCs set [emulator]
Station sensor-signal control PLCs set [emulator]
Train controller PLCs [emulator]
Electrical signal out
Electrical signal in
Railway system SCADA server
Trains system SCADA server
Trains monitor & control HMI
Railway monitor & control HMI
Maintenance laptops
Corporate Network
ICS [OT network ]
Railway HQ operator
Trains driver /operator
Production management workstation
ERP servers
Corporate IT servers
Users, staff and manager
IT management computers
IT engineer
ICS engineer
Mini Railway Cyber Range Network Diagram and Components View
Local HW-Engineering admin laptop
Field device admin
Ethernet TCP/IP
Ethernet TCP/IP and Modbus TCP
Modbus TCP and S7Comm
Train Monitor RTUs [emulator]

## Slide 3
Railway Physical-world Simulator
Electrical signal communication simulation module (10.0.10.100)
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1] I/O: 15/7
[Slave, Slot-2] I/O: 9/5
PLC-00
PLC-01
PLC-02
Railway track junction signaling control PLC network
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Railway track station signaling control PLC network
22 station sensor state (input to PLC)
10.0.10.10X
10.0.10.11X
Modbus IP: 192.168.100.1X/24
Modbus IP: 192.168.101.2X/24
Register read request and Coils set request
22 PLC coils state (output to signals )
Railway Track SCADA Monitor HMI(s)
Slave HMI(S) IP:192.168.10.10X
39 track sensors state ( input to PLC)
19 PLC coils ( output to signal)
HMI network 192.168.10.x
Master HMI IP: 192.168.10.100
Modbus Network 192.168.100.0/24
Slave HMI(s)
UDP data flow (simulate electrical signal )
Modbus-TCP data flow
Switch or Router
Legend
Register read request and Coils set request
Users
Railway engineer

## Slide 4
Railway Physical-world Simulator
Electrical signal communication simulation module (10.0.10.100)
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1] I/O: 15/7
[Slave, Slot-2] I/O: 9/5
PLC-00
PLC-01
PLC-02
Railway track junction signaling control PLC network
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Railway track station signaling control PLC network
22 station sensor state (input to PLC)
10.0.10.10X
10.0.10.11X
Modbus IP: 192.168.100.1X/24
Modbus IP: 192.168.101.2X/24
Register read request and Coils set request
22 PLC coils state (output to signals )
Railway Track SCADA Monitor HMI(s)
Slave HMI(S) IP:192.168.10.10X
39 track sensors state ( input to PLC)
19 PLC coils ( output to signal)
HMI network 192.168.10.x
Master HMI IP: 192.168.10.100
Modbus Network 192.168.100.0/24
Slave HMI(s)
UDP data flow (simulate electrical signal )
Modbus-TCP data flow
Switch or Router
Legend
Register read request and Coils set request
Users
Railway engineer
1
2
3
4
5
6
7
8
9

## Slide 5
Railway real-world Emulator
Electrical signal communication simulation module (10.0.10.100)
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
39 sensors input
19 signal coils output
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
22 station
Signal output
22 station
Sensors input
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
10 train throttle
input
10.0.13.10
10.0.12.10
10.0.11.10
Railway SCADA HMIs
Modbus Network 192.168.100.0/24
Modbus IP: 192.168.100.13
Modbus IP: 192.168.100.12
Modbus IP: 192.168.100.11
Master HMI IP: 192.168.10.100
Coils control request
Register control request
Coils control request
Register control request
Coils control request
Master HMI
Slave HMI(s)
Slave HMI IP: 192.168.10.10X
Register control
Coils control
Register data fetch
Coils data fetch
HMI network 192.16.10.x
Train Control panel
Modbus IP: 192.168.100.2xx
Coils control request
UDP data flow:
Modbus TCP data flow:

## Slide 6
Train Speed Reset
Train Emergency Stop
Train Sensor
Train Station
Railway Cross Signal
Green: Pass [off]
Red: Block [on]

## Slide 7
Real work sensor data
PCL coil output data
Database
Communication manager
PCL input data
PCL coil output data
ModBus TCP
PLC simulator VM
SCADA HMI data Visualization
Metro Control HMI

## Slide 8
Signal Trigger on sensor
Signal Trigger off sensor
Railway control signal
Use PLC to create a T Flip – Flop latching relay with signal trigger on has high priority

## Slide 9
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Station config file
Scenario config file
Init main UI (main thread)
Init PLC request handler (sub thread )
UI data controller (map manager)
Display UI map panel
Train power control panels
Display UI refresh loop
Components state data
Control event
PLC data controller (data manager)
Holding register data
Coil state change data
PLC Connector (UDP server)
PLC state data
Network
Other PLC modules
Other PLC modules
Other PLC modules
Use UDP to simulate the real-word electrical system wires connection
System auto controller ( if test mode )
All Plc connection and data update state

## Slide 10
Train
Scenario load drop down menu
Date and Time
Station
PLC connection state
Trains power control panels
Trains collision auto avoidance control
Train position sensors
Railway track signals

## Slide 11
Train control panel
Train power on Button
Train position reset button
Emergency Stop button (power cut off)
Train auto collision avoidance on/off control
Train auto collision avoidance OFF:
Behind train will “hit” the front stopped train directly and stop. An accident indicator will flash at the accident position
UI scenario :
Train auto collision avoidance ON:
Behind train will change speed to 0 to wait the front train if the train’s sensor detects a train in it front in the safety threshold distance.
UI scenario :
Step 1: click config dropdown menu and select “load scenario”
Step 2:When the Scenario selection window pop-up,
Click the Scenario you want to load
Step 3: Click “OK” to load to the real-world simulator

## Slide 12
Junction entrance block sensor
Junction Area
Junction entrance release sensor
T-flip-flop latching relay implemented by PLC ladder logic
Train entrance block signal
Step 1: When a train is entering the junction and trigger the entrance block sensor (sensor color change from grey to blue )
Operation Scenario 1: Junction block when train pass through
Step 2: Junction entrance block signal will turn on (red) to block the train on yellow track to enter the junction
Operation Scenario 1: Junction release when train leaving
Step 3: When a train is leaving the junction and trigger the entrance release sensor (sensor color change from grey to blue )
Step 4: Junction entrance block signal will turn OFF (green) to allow the train on yellow track to enter the junction
Physical wire
Junction’s Senor-Signal physical wire connection and operating logic

## Slide 13
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Real world connector (thread1)
Logic calculator (thread2)
Ladder logic bank
Modbus server (thread3)
Real world Communication loop
Register and coils state manager
real-world input sensor data
Holding register state change data
Coils state change data
real-world output signal data
Change Coils state
Read holing register state
Modbus request queue handling loop
Network
Network
UDP data flow
2D Railway[Metro] System Real-world Emulator
Railway[Metro] System SCADA-HMI

## Slide 15
Direct trigger latching relay implemented by PLC ladder logic
Train docking sensor
Train exit station block signal light
Operation Scenario 1: Train enter the station and trigger the docking sensor:
Operation Scenario 2: Station turn on train exit signal to stop the train for docking, also turn on the station enter block signal to avoid other trains enters the station:
Train enter station block signal light
Operation Scenario 3: When the train finished docking, turn off both signal light to allow train left the station:
Station waits another train dock:
Physical wire
Station’s Senor-Signal physical wire connection and operating logic

## Slide 16
Train speed sensor
Train power (moto)
PLC input connector
PLC output connector
Operation Scenario 1(Red) : Train power off, Train speed is 0 km/ h
Operation Scenario 2(Orange) : Train power on , Train speed is low (0 km/ h – 20km/h)
Operation Scenario 2(Green) : Train power on , Train speed is normal (56 km/ h – 90 km/ h)
Train’s Senor-Power physical wire connection and operating logic

## Slide 17
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Real world connector (thread1)
Modbus server (thread2)
Real world Communication loop
Register and coils state manager
real-world input sensor data
real-world output signal data
Change Coils state
Read holing register state
Modbus request queue handling loop
Network
Network
UDP data flow
2D Railway[Metro] System Real-world Emulator
Trains Control HMI

## Slide 18
Program start
Loading config files
Program system config file
Init main UI (main thread)
Init PLC Connector (sub thread )
UI data controller (map manager)
Display UI info panel
Train power control panels
Display UI refresh loop
PLC state data
Power Control event
PLC data controller (data manager)
Holding register data
Coil state change data
PLC client (Modbus TCP client)
PLC state data
Network
Trains Sensor-Power System Control PLC Simulator module
PLC state panels
Trains information
Modbus TCP data

## Slide 19
Trains information display grid
Turn train power ON button
Turn train power OFF button (emergency stop)
PLC state panel
PLC connection state
PLC coils state indicator
PLC holding register state indicator
Date & time
Critical information and error state display bar

## Slide 20
Emergency Stop button pressed (Mode-B) :
Train power off, Train totally stop[speed=0], Current cut off. Voltage range in (Normal , Max. permanent)
PLC speed sensor (Register) indicator OFF (grey).
PLC train motor power indicator OFF (white)
Train normal operation mode A-1 (docking/waiting):
Train power on, Train speed very low [<5km/h], Current drop low. Voltage range in (Min. permanent , Normal)
PLC speed sensor (Register) indicator OFF (grey).
PLC train motor power indicator ON (green)
Train normal operation mode A-2 (running)

## Slide 21
Program start
Loading config files
Program system config file
Init main UI (main thread)
Init PLC Connector (sub thread )
UI data controller (map manager)
Map display panel
PLC set 1 state display panels
Display UI refresh loop
PLC state data
PLC data controller (data manager)
Holding register data
Coil state change data
Junction PLC client (Modbus TCP client)
PLC state data
Network
Railway Junctions Sensor-Signal System Control PLC Simulator
PLC set 2 state display panels
Digital I/O Information
Modbus TCP data
Station PLC client (Modbus TCP client)
Modbus TCP data
Railway Stations Sensor-Signal System Control PLC Simulator
PLC state data
PLC state data

## Slide 22
Junction block sensor [with red dash line]
Junction block sensor [with green dash line]
Junction block signal ON [Red]
Junction block signal OFF [Green]
Junction release sensor triggered [ Yellow]
Junction block sensor triggered [ Yellow]
Train station docking sensor [Grey]
Train station docking sensor triggered [Yellow]
Train station signal [green]
PLC information
PLC coil voltage high
PLC coil voltage low
Digital input connected
Digital input empty
PLC register state voltage high
PLC register state voltage low
Digital output connected
Digital output empty

## Slide 23
Station triggered example
Step 1.0: In real-world emulator, train triggered the station docking sensor, Digital input signal change the register’s state
Step 2.0: PLC executes the ladder logic, turn on coils to change the digital output
Step 1.1 :Map station sensor changed to triggered state (yellow color)
Step 3: Real-world emulator signal turn on to block the train.
Step 2.0: Map station signal changed to block state (red color)

## Slide 24
Step 1.0: In real-world emulator, train triggered the junction entrance sensor, Digital input change the register’s state
Step 1.1: In the map the sensor will show triggered state (yellow color)
Step 2.0: PLC execute the ladder logic, then change the coil sate
Step 2.1: digital output will change the related signal connect to it to block the junction
Step 3.0: In real-world emulator, train triggered the junction release sensor, Digital input change the register’s state
Step 3.1: digital output will change the related signal connect to it to release the junction

## Slide 25
Railway Real-world Emulator VM/Node
10.0.10.100
Train Control PLC VM/VMs
10.0.10.13
Station Control PLC VM/VMs
Signal Control PLC VM/VMs
10.0.10.12
10.0.10.11
Real world electrical signal simulation subnet
Real world emulator program
PLC Simulator Program
PLC Simulator Program
PLC Simulator Program
Railway HMI program [master]
SCADA HMI Operation VM/Node
Railway HMI program
SCADA HMI Monitor VM/Node
SCADA HMI subnet
192.168.10.100
192.168.10.10X
192.168.11.10
192.168.11.1X
Train driver subnet
192.168.100.13
192.168.100.12
192.168.100.11
192.168.100.2xx
OT-Network
IT-Network
Train control program

## Slide 26
Corporate network [IT network]
Supervision network SCADA
Production network
Physical real world emulation network
Real world emulator
Track junction sensors-signals control emulators
Train station sensors-signals control emulators
Train emulators
Junction sensor-signal control PLCs set [emulator]
Station sensor-signal control PLCs set [emulator]
Train controller PLCs [emulator]
Electrical signal out
Electrical signal in
Railway system SCADA server
Trains system SCADA server
Trains monitor & control HMI
Railway monitor & control HMI
Maintenance laptops
Corporate Network
ICS [OT network ]
Railway HQ operator
Trains driver /operator
Production management workstation
ERP servers
Corporate IT servers
Users, staff and manager
IT management computers
IT engineer
ICS engineer
Railway[Metro] IT/OT System Security Test Platform Network Diagram and Components View
Local HW-Engineering admin laptop
Field device admin
Ethernet TCP/IP
Ethernet TCP/IP and Modbus TCP
Modbus TCP

## Slide 27
Corporate network [IT network]
Supervision network SCADA
Production network
Physical real world emulation network
Track junction sensors-signals control emulators
Train station sensors-signals control emulators
Train emulators
Junction sensor-signal control PLCs set [emulator]
Station sensor-signal control PLCs set [emulator]
Train controller PLCs [emulator]
Electrical signal out
Electrical signal in
Railway system SCADA server
Trains system SCADA server
Trains monitor & control HMI
Railway monitor & control HMI
Maintenance laptops
Corporate Network
ICS [OT network ]
Railway HQ operator
Trains driver /operator
Production management workstation
ERP servers
Corporate IT servers
Users, staff and manager
IT management computers
IT engineer
ICS engineer
Railway[Metro] IT/OT System Security Test Platform Network Diagram and Components View
Local HW-Engineering admin laptop
Field device admin
Ethernet TCP/IP
Ethernet TCP/IP and Modbus TCP
Modbus TCP

## Slide 28
Network Map Info:
Supervision network SCADA.(For OT attack test )
Network Map Info:
Physical wire connection emulation network
OpenStack provider network used as the Green team development network
Railway system cyber range system on OpenStack
Next Step work:
Add one subnet (jump host link to OT network) with 10 small empty ubuntu VMs named as HR server, Web billing server , finance server, file server, email server … to simulate the corporate network.
Add one subnet (jump host link to corporate network) with 5 small empty ubuntu VMs named as DC server, NTP server , DNS server, VPN server … to simulate the DMZ network.

## Slide 29
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
PLC0 Q0.0
S-we-0
PLC0 Q0.2
S-we-2
PLC0 Q0.4
S-we-4
PLC0 Q0.6
S-we-6
PLC1 Q0.0
S-we-7
PLC0 Q0.1
S-we-1
PLC0 Q0.5
S-we-5
PLC0 Q0.3
S-we-3
PLC1 Q0.1
S-ns-0
PLC1 Q0.2
S-ns-1
PLC1 Q0.3
S-ns-2
PLC1 Q0.4
S-ns-3
PLC1 Q0.5
S-cc-0
PLC1 Q0.6
S-cc-1
PLC2 Q0.0
S-cc-2
PLC2 Q0.1
S-cc-3
PLC2 Q0.2
S-cc-4
PLC2 Q0.3
S-cc-5
PLC2 Q0.4
S-cc-6
Ladder Diagram set information:
PLC number: 3
Holding register: 39
Coil: 19
Total ladder diagram: 19
Ladder diagram detail:
Railway Signal System PLC set ladder logic

## Slide 30
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
10.0.12.10
Ladder Diagram set information:
PLC number 3
Holding register: 22
Coil: 22
Total ladder diagram: 22
Ladder diagram detail:
Railway Station system PLC set ladder logic

## Slide 31
Train Control PLC Configuration
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
Ladder Diagram set information:
PLC number 2
Holding register: 0
Coil: 10
Total ladder diagram: N.A (direct control)
Ladder diagram detail: N.A
t0
10ms
Fetch PLC Input sensor voltage and set the register
t2
Execute the ladder logic
t1: Inject false register value to overwrite sensor reading
10ms
80ms
Real PLC with 20ms clock cycle
PLC Emulator with 80ms clock cycle
t3
t4
Low frequence false data injection attack not success on real PLC because the false data is overwritten by the sensor data read on t2 and t3.
False data injection attack success, the PLC execute the ladder logic based on the false injected sensor volage value.

## Slide 32
Train State Panel
Train ID
Train DC power state
Train DC Current(A)
Train DC Voltage(V)
Train current speed gauge
Train average speed indicator
Train poser state reset button
Train emergency stop button
Train state history table
Train’s Control PLC state panel
Train’s collision avoidance overload control

## Slide 33
Junction PLC
Station PLC
Modbus-TCP
Real word junction sensors and signal
Real word station sensors and signal
UDP simulate electrical signal
UDP simulate electrical signal

## Slide 34
Real word trains PLC throttle and brake control
UDP simulate electrical signal
Modbus-TCP
Train Control PLC